## Slide 1: FNAL Test Beam Analysis: Spatial Resolution Studies
Kondo Gnanvo

## Slide 2
UVa GEMs @ FNAL Test Beam: 120 GeV Proton Beam
SBS1
TRK_4: SBS2
EIC-SoLID
TRK_0
TRK_1
TRK_2
Space points of the GEMs chambers from 50K events.
DAQ rate ~ 400 Hz, 3 APV25 time samples
Beam profile on TRK_1

## Slide 3
Position correlation of the Trackers
X-coordinates
Y-coordinates
Tracker0 vs. Tracker1
X-coordinates
Y-coordinates
Tracker0 vs. Tracker2

## Slide 4
Tracking and Residuals: Exclusive SBS1
Good event: single hit in each X and Y direction for all 4 Trackers (3 samll GEMs and SBS2)
Tracking: Linear fit in X and Y using the single hit from the 4 trackers  SBS1 data excluded
Residual distribution: (XSBS1 – Xtrack) and (YSBS1 – Ytrack)
sx = 65 mm
sy = 76 mm

## Slide 5
Tracking and Residuals: Inclusive SBS1
sx = 52 mm
sy = 60 mm
Good event: single hit in each X and Y direction for all 4 Trackers (3 samll GEMs and SBS2)
Tracking: Linear fit in X and Y using the single hit from the 4 trackers as well as SBS1hit  inclusive SBS1.
Residual distribution: (XSBS1 – Xtrack) and (YSBS1 – Ytrack)

## Slide 6
Spatial Resolution of SBS1
sx = 58 mm
sy = 68 mm
Combined distribution : Exclusive and Inclusive residual distribution are merged
Resolution: Width (sresolution) of the Gaussian fit to the combined residual distribution
Resolution: sresolution = sqrt (sexclusive × sinclusive)

## Slide 7
Tracking and Residuals: exclusive EIC-SoLID
sx = 413 mm
sy = 220 mm
Good event: single hit in each X and Y direction for all 4 Trackers (3 samll GEMs and SBS2)
Tracking: Linear fit in X and Y using the single hit from the 4 trackers
Residual distribution: (XEIC-SoLID – Xtrack) and (YEIC-SoLID – Ytrack)